## Slide 1: Conceptual Dynamics
Part II: Particle Kinematics
Chapter 3
Kinematics of Particles
Plane Curvilinear Motion
n-t Coordinates

## Slide 2: n-t Coordinate System

## Slide 3: n-t coordinate system
Solving for the acceleration of Car A would be difficult using x-y coordinates.
  x-y is good for straight line motion.

## Slide 4: n-t coordinate system
n-t coordinates are more natural for curved paths that are known.

## Slide 5: Normal & Tangential Coor. Sys.
Used when the path of the particle is known.
Body fixed coordinate frame
  Attached to and moves with the particle.

## Slide 6: Normal & Tangential Coor. Sys.

## Slide 7: Normal & Tangential Coor. Sys.
t - axis: The positive t – axis is in the direction of motion, tangent to the path curve.

## Slide 8: Normal & Tangential Coor. Sys.
n – axis: The positive n – axis is perpendicular to the t – axis and is directed toward the center of curvature.

## Slide 9: Example 3.3-1
Draw the n-t axes for the two particles.
  C denotes the center of curvature.

## Slide 10: Example 3.3-1
Draw the n-t axes for the two particles.
  C denotes the center of curvature.

## Slide 11: Velocity

## Slide 12: Velocity
Velocity is the time rate of change of position.
Velocity is always tangent to the path.
  t-axis is always tangent to the path.

## Slide 13: Example 3.3-2
Derive the following speed equation with the help of the figure.

## Slide 14: Example 3.3-2
What is the general calculus equation for the velocity?

## Slide 15: Example 3.3-2
What is the length of ds?

## Slide 16: Example 3.3-2
Derive the velocity equation.

## Slide 17: Example 3.3-2
Derive the velocity equation.

## Slide 18: Acceleration

## Slide 19: Acceleration
Acceleration: Time rate of change of velocity.
Use the product rule to take the derivative of the velocity.
Does like ?
No. The t – axis changes direction.

## Slide 20: Acceleration
Acceleration: Time rate of change of velocity.
This is not a very useful form of the acceleration equation. We need to find out what equals.

## Slide 21: Acceleration
We need to know both the magnitude and direction of

## Slide 22: Acceleration
Direction of det /dt : As ds becomes smaller and smaller, will begin to point in what direction?

## Slide 23: Acceleration
Direction of det /dt : As ds becomes smaller and smaller, will begin to point in what direction?

## Slide 24: Acceleration
Magnitude of : When ds becomes infinitesimally small, can be estimated by the arc length between and .
What is the magnitude
of ?

## Slide 25: Acceleration
Magnitude of : When ds becomes infinitesimally small, can be estimated by the arc length between and .
What is the magnitude
of ?
dq

## Slide 26: Acceleration
Take the time derivative of both sides.

## Slide 27: Acceleration
Use the velocity equation to determine the value of ?

## Slide 28: Acceleration

## Slide 29: Acceleration
A particle’s acceleration is always nonzero if the particle is moving on a curve, even if its speed is constant. Why?

## Slide 30: Acceleration
A particle’s acceleration is always nonzero if the particle is moving on a curve, even if its speed is constant. Why?
Velocity changes
direction.
A constant speed
only means that
at = 0.

## Slide 31: Acceleration
What does represent in the above equation?

## Slide 32: Acceleration
What does represent in the above equation?
The increase in speed.
Car: Stepping on the gas pedal.

## Slide 33: Acceleration
What does represent in the above equation?

## Slide 34: Acceleration
What does represent in the above equation?
Acceleration due to a change in direction.
Car: Turning the steering wheel.

## Slide 35: Important Equations
Used if the path curve is a
given function ( f (x) )

## Slide 36: Circular Motion

## Slide 37: Circular Motion
Consider a car that travels around a circular test track of radius r.

## Slide 38: Circular Motion
The n-t coordinate velocity and acceleration equations are given.
What remains constant when considering circular motion?

## Slide 39: Circular Motion
The radius is constant (r = r).

## Slide 40: Circular Motion
We can rearrange these equation further.

## Slide 41: Conceptual Example 3.3-3
Consider the ski jumper shown in the figure. Neglect surface friction and air resistance. Determine the direction of the velocity and acceleration of the skier at position A, B and C. Use the arrow diagram to describe the direction.

## Slide 42: Conceptual Example 3.3-3
What direction is the acceleration of the skier at position A, B and C.

## Slide 43: Conceptual Example 3.3-3
What direction is the acceleration of the skier at position A, B and C.
A

## Slide 44: Conceptual Example 3.3-3
What direction is the acceleration of the skier at position A, B and C.
A
B

## Slide 45: Conceptual Example 3.3-3
What direction is the acceleration of the skier at position A, B and C.
A
C
B

## Slide 46: Conceptual Example 3.3-4
Consider a ball moving at 5 m/s, but in the following situations represented in the figure. Rank the situations in order of largest to smallest ball acceleration magnitude for the instant represented in the figure.

## Slide 47: Conceptual Example 3.3-4
Largest
Next
Next
Next
Next
Smallest

## Slide 48: Conceptual Example 3.3-4
Largest
Next
Next
Next
Next
Smallest
F
E
D, C
B
A
a = 9.81 m/s2
a = <9.81 m/s2
a = 0 m/s2
a = <9.81 m/s2
a = 25 m/s2
a = 27 m/s2

## Slide 49: Conceptual Example 3.3-5
It is known that the total amount of acceleration that a racecar tire can achieve before skidding is limited. Therefore, which of the following paths should a racecar driver take through a curve in order to maximize the amount of speed that she can carry through the curve?

## Slide 50: Conceptual Example 3.3-5
Which of the following paths should a racecar driver take through a curve in order to maximize the amount of speed that she can carry through the curve?

## Slide 51: Conceptual Example 3.3-5
Which of the following paths should a racecar driver take through a curve in order to maximize the amount of speed that she can carry through the curve?

## Slide 52: Example Problems
EP3.3-6
EP3.3-7 (Video)
EP3.3-8
EP3.3-9