## Slide 1: Conceptual Dynamics
Part II: Kinematics of Particles
Chapter 3
Kinematics of Particles
Plane Curvilinear Motion
Polar coordinates

## Slide 2: Polar Coordinate System

## Slide 3: Polar Coordinate System
The Polar Coordinate System is defined by the coordinates r and q.
The r and q axes are attached to and move with the particle.

## Slide 4: Radial coordinate & the r-axis
Radial Coordinate (r) The distance from the origin of the x-y coordinate system to the particle.

## Slide 5: Radial coordinate & the r-axis
r – axis: Parallel to r and points away from the origin.

## Slide 6: Transverse Coor. & the q-axis
Transverse Coordinate (q) The angle between the positive x-axis and r.

## Slide 7: Transverse Coor. & the q-axis
q – axis: Perpendicular to the r – axis and is positive in the direction of increasing q.

## Slide 8: Example 3.4-1
Draw the r-q axes, and the radial and transverse coordinates for both positions of the particle shown.

## Slide 9: Example 3.4-1
Draw the r-q axes, and the radial and transverse coordinates for both positions of the particle shown.

## Slide 10: Position Velocity Acceleration

## Slide 11: Position
Position (r) The vector that starts at the origin of the x-y coor. system and points to the particle.

## Slide 12: Velocity
Velocity (v)
  r-q axis are body-fixed.

## Slide 13: Acceleration
Acceleration (a)
  r-q axis are body fixed.

## Slide 14: Conceptual Example 3.4-2
For the following situations, write an expression for the velocity and acceleration in polar coordinates.
  A car travelling on a circular track.

## Slide 15: Conceptual Example 3.4-2
For the following situations, write an expression for the velocity and acceleration in polar coordinates.
  A car travelling on a circular track.

## Slide 16: Conceptual Example 3.4-2
For the following situations, write an expression for the velocity and acceleration in polar coordinates.
  A car on a Ferris wheel turning at a constant rate.

## Slide 17: Conceptual Example 3.4-2
For the following situations, write an expression for the velocity and acceleration in polar coordinates.
  A car on a Ferris wheel turning at a constant rate.

## Slide 18: Conceptual Example 3.4-2
For the following situations, write an expression for the velocity and acceleration in polar coordinates.
  Body A held by the end of an articulating robotic arm.

## Slide 19: Conceptual Example 3.4-3
If the slotted bar is rotating counter-clockwise at a decreasing rate, what are the signs of the first two time derivatives of q and the first derivative of r?
  Positive?
  Negative?

## Slide 20: Conceptual Example 3.4-3
If the slotted bar is rotating counter-clockwise at a decreasing rate, what are the signs of the first two time derivatives of q and the first derivative of r?
  Positive?
  Negative?

## Slide 21: Polar vs. n-t Coordinates

## Slide 22: r-q versus n-t
It is important to note that the r-q and n-t coordinate systems do not necessarily coincide.

## Slide 23: Example 3.4-4
Draw the r-q and n-t axes.
Include the position and velocity vectors, and the transverse coordinate.

## Slide 24: Example 3.4-4
Draw the r-q and n-t axes.
Include the position and velocity vectors, and the transverse coordinate.

## Slide 25: Example 3.4-4
Include the position and velocity vectors, and the transverse coordinate.

## Slide 26: r-q versus n-t
In the n-t coordinate system, the velocity has only a t component.
In the polar coordinate system, the velocity usually has both an r and q components.

## Slide 27: Important Equations
= w = Angular velocity (rad/s)
= a = Angular acceleration (rad/s2)

## Slide 28: Example Problems
EP3.4-5
EP3.4-6 (Video)